## Slide 1: Introduction to Software Defined Networks (SDN)
Irfan Ali
Slides adapted from Prof. Berk Canberk

## Slide 2: Outline
Motivation- 1 (This lecture)
  Centralizing the “routing/forwarding” logic
  Centralizing “middleboxes”: Firewall and NAT
Motivation -2 (Next two lectures)
  Data-center networks
  Network-virtualization and multi-tenancy support

## Slide 3: Traditional Computer Networks
Data plane:
Packet streaming
  Forward, filter, buffer, mark,
  rate-limit, and measure packets
Notes: Maybe this is a better picture… though need some details of what happens in each plane… like in next slides… or, have both?

## Slide 4: Traditional Computer Networks
  Track topology changes, compute routes, install forwarding rules
Control plane:
Distributed algorithms
Notes: Maybe this is a better picture… though need some details of what happens in each plane… like in next slides… or, have both?

## Slide 5: Traditional Computer Networks
  Collect measurements and configure the equipment
Management plane:
Human time scale
Notes: Maybe this is a better picture… though need some details of what happens in each plane… like in next slides… or, have both?

## Slide 6: Example: Traditional Network Router
Router can be partitioned into control and data plane
  Management plane/ configuration
  Control plane / Decision: OSPF (Open Shortest Path First)
  Data plane / Forwarding
Adjacent Router
Router
Management/Policy plane
Configuration / CLI / GUI
Static routes
Control plane
OSPF
Neighbor table
Link state database
IP routing table
Forwarding table
Data plane
Data plane
Control plane
OSPF
Adjacent Router
Data plane
Control plane
OSPF
Control Plane
User Plane
Distributed automaton

## Slide 7: Problems with traditional networks
Trying to “program” a particular behavior is an extremely complicated task.
  Several hundred lines of configuration on each interface.
  Several parameters: routing, forwarding, keep-alives.
Several very tough tradeoffs
  Fast recovery vs keep-alive traffic vs false positives
Each router vendor has its own configuration language (command line interface)
Features between router vendors do not work that easily.
Every new feature from router vendor costs $$$$.

## Slide 8: Software Defined Networking (SDN)
API to the data plane
(e.g., OpenFlow)
Logically-centralized control
Switches
Smart,
slow
Dumb,
fast

## Slide 9
Make it easy to “Program the network”
  Centralize the control logic of the network
  Use commodity hardware for user-plane
Main drivers for SDN
  Reduce cost of data-center networks
  Network Multi-tenancy: Enable ability to share network with multiple tenants each with their own network topology.
Software Defined Networking = Program the Network, Cheaply

## Slide 10: Basic SDN Motivation!
Simpler management
  No need to “invert” control-plane operations
Faster pace of innovation
  Less dependence on vendors and standards
Easier interoperability
  Compatibility only in “wire” protocols
Simpler, cheaper equipment
  Minimal software

## Slide 11: What “logic/box” is being centralized?
Routing logic/Router
  Match: longest destination IP prefix
  Action: forward out a link
Switching logic/Switch
  Match: destination MAC address
  Action: forward or flood
Firewall logic/Firewall
  Match: IP addresses and TCP/UDP port numbers
  Action: permit or deny
Address-Port translation logic/NAT
  Match: IP address and port
  Action: rewrite address and port

## Slide 12: SDN High Level Architecture
South-bound Interface
North-bound Interface
Data Plane
Control Plane

## Slide 13
Control and Data Planes Isolation
Applications Layer:
SDN applications
Business applications
Global Network View
North-Bound APIs
South-Bound APIs
SDN Controller
QoS
Routing
Monitoring
Traffic Eng..
Control-Plane Layer:
SDN Controller(s)
North-bound APIs
South-bound APIs (e.g., OpenFlow protocol)
Data-Plane Layer:
OpenFlow(OF) Switches
Routers
Other Infrastructure elements

## Slide 14
OpenFlow Switching
Controller
PC
Hardware
Layer
Software
Layer
OpenFlow Table
MAC
src
MAC
dst
IP
Src
IP
Dst
TCP
sport
TCP
dport
Action
OpenFlow Client
*
*
5.6.7.8
*
*
*
port 1
port 4
port 3
port 2
port 1
1.2.3.4
5.6.7.8
14

## Slide 15
OpenFlow Switching
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
00:1f:..
*
*
*
*
*
*
*
port6
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
*
*
*
22
drop
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
5.6.7.8
*
*
*
port6
Switching Use Case
Routing Use Case
Firewall Use Case

## Slide 16: Openflow Table

## Slide 17: Matching (OpenFlow v. 1.0)
Packet header fields matched against one of N tables
If no match, packet is sent to controller
Otherwise, switch performs action
https://www.opennetworking.org/images/stories/downloads/sdn-resources/onf-specifications/openflow/openflow-spec-v1.0.0.pdf

## Slide 18: OF Tables
Packet Flow through the processing pipeline

## Slide 19
Operation and Flow Management
All incoming flow are received by the OF switches in Data Plane
In switch, the destination addresses of each flows are checked from Flow Table Pipeline
If it is matched, the actions in figure are performed
If it is not matched, that flow is called as “newcomer” flow and first packet is sent to Controller
Controller decides suitable solution, updates the flow entry and assigns a forwarding rule for this newcomer flow
-G. Secinti, B. Canberk, T. Duong, L. Shu., ‘Software Defined Architecture for VANET: A Testbed Implementation with Wireless Access Management’, IEEE Communications Magazine, 2017.

## Slide 20
Operation and Flow Management
-G. Secinti, B. Canberk, T. Duong, L. Shu., ‘Software Defined Architecture for VANET: A Testbed Implementation with Wireless Access Management’, IEEE Communications Magazine, 2017.

## Slide 21: The Actual Flow Table Looks Like
QoS
Protocol

## Slide 22: OpenFlow Table: Basic Actions
All To all interfaces except incoming interface.
Controller Encapsulate and send to controller.
Local send to its local networking stack.
Table Perform actions in the next flow table (table chaining or multiple table instructions).
In_port Send back to input port.
Normal Forward using traditional Ethernet.
Flood Send along minimum spanning tree except the incoming interface.

## Slide 23: OpenFlow Table: Basic Stats
Provide counter for incoming flows or packets.
Information on counter can be retrieved to control plane.
Can be used to monitor network traffic.

## Slide 24: Main Components of an OF Switch

## Slide 25: Main Components of an OF Switch
Control Channel: The aggregation of components of an OpenFlow logical switch that manages communication with controllers. The control channel includes one OpenFlow channel per OpenFlow controller.
  OpenFlow Channel: Interface between an OpenFlow switch and an OpenFlow controller, used by the controller to manage the switch.
Datapath: The aggregation of components of an OpenFlow logical switch that are directly involved in traffic processing and forwarding. The datapath includes the pipeline of flow tables, the group table and the ports.
  Group: List of action buckets and some means of choosing one or more of those buckets to apply on a per-packet basis.
  Meter: Switch element that can measure and control the rate of packets. The meter triggers a meter band if the packet rate or byte rate passing through the meter exceeds a predefined threshold. If the meter band drops the packet, it is called a Rate Limiter.
Pipeline: the set of linked flow tables that provide matching, forwarding, and packet modification in an OpenFlow switch.
  Flow Entry: an element in a flow table used to match and process packets. It contains a set of match fields for matching packets, a priority for matching precedence, a set of counters to track packets, and a set of instructions to apply
  Flow Table: a stage of the pipeline. It contains flow entries.

## Slide 26: Flow Tables and Entries
match fields: to match against packets. These consist of the ingress port and packet headers, and optionally other pipeline fields such as metadata specified by a previous table.
priority: matching precedence of the flow entry.
counters: updated when packets are matched.
instructions: to modify the action set or pipeline processing.
timeouts: maximum amount of time or idle time before flow is expired by the switch.
cookie: opaque data value chosen by the controller. May be used by the controller to filter flow entries affected by flow statistics, flow modification and flow deletion requests. Not used when processing packets.
flags: flags alter the way flow entries are managed, for example the flag OFPFF_SEND_FLOW_REM triggers flow removed messages for that flow entry.

## Slide 27
Operation and Flow Management
Control Link
Data Link
Forwarding path
Host
Host
1
2
3
3
3
4
4
Controller
4
2
3
4
Path Request
Installation of Rules
New FDN
Example of Flow Management
1
2
3
If the new flow does not match the flow entries at the Flow Tables
Controller computes the path for the new flow, and sends the flow entry to all OF switches
Send the first packet of the new
flow to the controller
4
New Flow Arrival
Path Request
Installation of Rules
New Flow is forwarded to destination
-M. Erel, Z. Arslan, Y. Ozcevik, B. Canberk, ‘Grade of Service based Adaptive Flow Management for Software Defined Heterogeneous Networks’, Computer Networks (Elsevier), 2015.
-M. Erel, Z. Arslan, Y. Ozcevik, B. Canberk, ‘Software-Defined Wireless Networking’, Elsevier, 2014.

## Slide 28
OpenFlow Switching
Controller
PC
OpenFlow Switch
OpenFlow Switch
OpenFlow Switch
Alice’s code
Decision?
OpenFlow
Protocol
Alice’s Rule
Alice’s Rule
Alice’s Rule
OF in action!

## Slide 29: Openflow Protocol Versions
Source: Kreutz et al.: Software-Defined Networking: A Comprehensive Survey, Proceedings of IEEE 2015

## Slide 30: Openflow enabled hardware and software
Source: Kreutz et al.: Software-Defined Networking: A Comprehensive Survey, Proceedings of IEEE 2015

## Slide 31: Open vSwitch
The Open vSwitch is a virtual switch that's available as open source under the Apache 2.0 license.
Open vSwitch supports the leading open source hypervisor solutions, including Kernel-based VM (KVM), VirtualBox, Xen, and XenServer. It's also a drop-in replacement for the current Linux bridge module.
Open vSwitch consists of a switch daemon and companion kernel module that manages the flow-based switching. A variety of other daemons and utilities also exist for managing the switch (particularly from the perspective of OpenFlow).
Source: https://www.ibm.com/developerworks/linux/library/l-virtual-networking/